## Slide 1: Plant Monitor Sketches
Mandy Ma Dongyi
CE Lab, CASA UCL

## Slide 2: Contents
Plant Monitor Demonstration
Live GitHub Repository
Live Data in MQTT Explorer

## Slide 3: Changes have been taken
1. On GitHub, delete test and useless repositories and then build local repository then publish to GitHub.com, write code locally and push changes into cloud.
2. On codes, rename all scripts used by their fucntion and order them with number. Re-write the overiew comments and add on detailed comments based on the fuctions of each part and where the codes were modified during workshop.
3. Change the delay from 500 to 50 and remove unnecessary delay to save some waiting time used in fetching data
4. Change upload speed of Arduino to 921600 to save some time for compliling scripts.
5. Add a if-else conditonal function to test moisture and if the moisture is below 100, returns am I thirsty? = yes. Otherwise return no.
6. Use secondChanged instead of minutechanged to fetch data and push to mqtt every second rather than every minute.

## Slide 4: Mistakes and Solutions
Mistakes | Solutions
serial monitor not showing meaningful words | Set the frequency to 115200
Failed to connect feather board to Wi-Fi | Check SSID password carefully with upper case and lower case
Failed to publish data in MQTT | Change to port 1884 (1883 is read only)
Too many software running | Close wechat, use command shift and 5 to do screenshot
Physical circuit not working | Remotely connect feather board to give more space for resistors and cables
Test moisture data too low | Water the plant

## Slide 5: Mistakes and Solutions
Mistakes | Solutions
Slodering wrong direction and physical position | Melt it and pull out then re-do soldering carefully
Error arduino_secrets.h: No such file or directory | Remember to put arduino_secrets.h: in the same file with the script it is encrypting for
Add if-else function failed to return a feedback result | Use the format ("student/CASA0014/plant/ucfndma/moisture", msg)
InfluxDB Error: Bad Request | 
Forgot to include gitignore and license in my github | Rembember next time when setting github

## Slide 6: Future actions
1. Figure out data visualization problem
2. Send txt message to my phone saying that I am thisrty!
3. Auto-water and hardware assemblying.